## Slide 1: Carrier Grade Minimalist Multicast (CGM2) using Bit Index Explicit Replication (BIER) with Recursive BitString Structure (RBS) Addresses IETF 112 / INTAREA
draft-eckert-bier-cgm2-rbs-00
Toerless Eckert (tte@cs.fau.de) Futurewei USA
Based on design/work from Sheng Jiang, Xu Bing, Yan Shen, Meng Rui, Wan Junjie and Wang Chuang {jiangsheng|bing.xu|ynshen|mengrui|wanjunjie2|wangchuang}@huawei.com

## Slide 2: Why INTAREA
Why not ? (is IntArea only for Unicast ? ;-)
To inform INTAREA of a great example, how further work on more intelligent (variable length) addressing helps to solve currently worked on routing problems better!
  Some call (“locator type”) addresses forwarding instructions (i like that too)
  IMHO whatever we call them, it is still routing

## Slide 3: What is wrong with BIER-TE ?
BIER-TE is the best multicast forwarding solution for its target constraints:
  BIER per flow/tree stateless forwarding with added tateless traffic steering…
  When we can only reuse the pre-existing BIER-TE ”flat-bitstring”
  and only no…minimal changes to BIER forwarding algorithm.
But this comes at undesirable limitations / complexities:
N-bit bitstring can address only fixed set of N-M BFER (e.g.: N=256)
  Because every bit of address is statically assigned to an adjacency (e.g.; BFER)
  M is number of bits needed to ’steer’ packets (BFR). Also fixed, potentially sub-part of topo.
  Same static mapping issues exist in BIER, but less severe
Result (as seen from BIER-TE draft):
  Design complexities minimizing required M bits (LAN, hub&spoke, p2p, overlay topologies, …). Controller and network operator.
  Larger number of copies with different bitstrings to reach arbitrary subset of BFER in large network
  OPS and CONTROLLER COMPLEXITY, less TRAFFIC EFFICIENCY for FORWARDING PLANE SIMPLICITY.

## Slide 4: Carrier-Grade Minimalist Multicast (CGM2) Deployment Simplicity Vision
Unicast encap
Encapsulation format ：
Multicast encap
Payload
CGM2 Router
Unicast-Only Router
Source
Client1
Client2
Client3
Client4
A
B
C
D
E
F
G
H
Controller
Recipient
Recipient
Recipient
Forward multicast traffic
Control signaling traffic
Fix the bitstring addressing issue
Eliminate duplication: IP multicast on top of bitstring forwarding (“overlay”)
  End-to-end integration with controller plane
Complete TE services via controller plane and forwarding plane
  Deterministic Latency, Path Selection (Steiner, diverse, …)

## Slide 5
BitString for R
Recursive Unit 1
…
Recursive Unit
Addressing Field
Recursive Bitstring Structure
Multicast Packet：
Fixed Field
Total len
rsv
Padding
L1
…
Ln-1
R
1
2
3
4
n
…
1
2
3
4
m
…
Recursive Bitstring Structure (RBS)
Recursive Unit 2
Recursive Unit n
BitString for 1
Recursive Unit 1
…
Addressing Field
Recursive Unit 2
Recursive Unit m
Fixed Field：
  Total len： indicate the total length of the Recursive Unit, Filed length can be set flexibly to 8/16/32, with bit/byte/word. Padding is not included.
  Rsv: Reserved Fields
Recursive Unit：
  Bitstring：instructs a node to locally duplicate packets and forwarding – like a BIER-TE bitstring (but without complex options)
  Addressing Field：length of ‘child’ recursive units .
  Recursive Unit：has the same structures as the unit it sits in.
Padding (Optional)：Used for alignment to byte (or larger).
Recursive Unit
5

## Slide 6
B
C
D
E
R
S
Client1
Client2
Client3
Client4
B:01
R:011
S:011
C:001
D:0001
E:001
Len=10
Encapsulation to B
Recursive unit0
Total_len:26
Padding(6bit)
Recursive Unit B
R:011
S:011
C:001
D:0001
E:001
Len=10
Recursive unit0
Recursive unit1
Encapsulation to R
Total_len:24
Recursive Unit R
S:011
C:001
D:0001
Encapsulation to S
Recursive unit1
Recursive unit0
Total_len:10
Padding(6bit)
Recursive Unit S
C:001
Encapsulation to C
Total_len:3
Padding(5bit)
D:0001
Encapsulation to D
Total_len:4
Padding(4bit)
E:001
Encapsulation to E
Total_len:3
Padding(5bit)
Client2
Client3
Client4
Client1
1
1
Index | Next hop
0 | client1
1 | R
Bitmap(B)
Forwarding table(B)
0
1
1
1
1
1
Bitmap(R)
Forwarding table(R)
0
1
1
Index | Next hop
0 | B
1 | S
2 | E
1
1
1
Index | Next hop
0 | R
1 | C
2 | D
Bitmap(S)
Forwarding table(S)
0
1
1
1
1
1
Index | Next hop
0 | S
1 | D
2 | client2
Bitmap(C)
Forwarding table(C)
0
0
1
Multicast route identifier：
  Define the local bitmap。
  Each bit corresponds to a multicast object, which denote the direct delivery destination of multicast packet.
Forwarding table：
  Each table entry corresponds to a bit in the bitmap.
  Instruct the forwarding method to the corresponding multicast object (outgoing interface, next hop address, etc.)
Unicast Packet
Unicast Packet
Unicast Packet
Example:
6
The bug in this example is left as an exercise to the reader

## Slide 7
Simplifications / Performance Enhancements
Naturally no need for loop prevention measures (as in BIER/BIER-TE) (no clear bits)
No need to split up topology into different SI and/or multiple SD bitstrings
No (or much smaller) need to create optimized bit semantics.
  Just use all adjacencies of topology and/or shortest tunnel adjacencies over unicast-routers.
Especially for ‘sparse’ (small number of BFER) distributions
  Can encode any subset and steering in single RBS address == single packet packet
  If majority of packet have sparse receiver sets. Duplicate packet reduction maximized.
When total number of BFR too large for desired max RBS address structure (eg: > 512 bit ?)
  Controller can arbitrary duplicate/split distribution tree to create multiple packets for ‘sub-trees’.
7

## Slide 8
Forwarding Pseudocode
void ForwardRBSPacket (Packet)
RBS = GetPacketMulticastAddr(Packet);
Total_len = RBS;
Rsv = Total_len + length(Total_Len);
BitStringA = Rsv + length(Rsv);
AddressingField = BitStringA + BIFT.entries;
// [1] calculate number of recursive bits set in BitString
CopyBitString(*BitStringA, *RecursiveBits, BIFT.entries);
And(*RecursiveBits,*BIFTRecursiveBits, BIFT.entries);
N = CountBits(*RecursiveBits, BIFT.entries);
// Start of first RecursiveUnit in RBS address
// After AddressingField array with 8-bit length fields
RecursiveUnit = AddressingField + (N - 1) * 8;
RemainLength = *Total_len - length(Rsv) - BIFT.entries;
Index = GetFirstBitPosition(*BitStringA);
while (Index) {
PacketCopy = Copy(Packet);
if (BIFT.BP[Index].recursive) {
if(N == 1) {
RecursiveUnitLength = RemainLength;
} else {
RecursiveUnitLength = *AddressingField;
N--;
AddressingField += 8;
RemainLength -= RecursiveUnitLength;
RemainLength -= 8; // 8 bit of AddressingField
}
RewriteRBS(PacketCopy, RecursiveUnit,
RecursiveUnitLength);
SendTo(PacketCopy, BIFT.BP[Index].adjacency)
RecursiveUnit += RecursiveUnitLength;
} else {
DisposeRBSheader(PacketCopy);
SendTo(PacketCopy, BIFT.BP[Index].adjacency);
}
Index = GetNextBitPosition(*BitStringA, Index);
}
8

## Slide 9
Other thoughts
Natural variable length address (structure)
  Compared to naturally fixed-size in BIER/BIER-TE
Forwarding plane complexity
  Basic Bitstring replication the same as BIER-TE (only simple subset of adjacencies required)
  Main added work:
    For each R)eplicating adjacency: locate offset/length of Recursive Unit for adjacency, rewrite RBS to that Recursive Unit
TBD: stochastical analysis/comparison of efficiency (#copies), compared to BIER/BIER-TE
  Wide comparison space…
Packet encoding
  Not purpose of this draft
  Could just use RFC8296 and be considered ‘yet another BIFT mode’ (BIER, BIER-TE, BIER-RBS)
  Or any other encap if more desirable / applicable

## Slide 10: THE END